## Slide 1: Application Performance Tuning on POWER9- with Compilers — Dr. Archana Ravindar (@aravind5@in.ibm.com)
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation Supercomputing‘ 2019, Denver

## Slide 2: Contents
Part One
Introduction and scope 03
Salient Features of POWER9 04
Tools used in the Presentation 06
Part Two
Optimizing Front End Performance 07
Part Three
Optimizing Back End performance 11
Additional ways of Tuning Performance 18
Compiler Flag Comparison – XL, GCC, Clang 19
Summary 20
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation

## Slide 3: Scope of the Presentation
Outline Tuning strategies to improve performance of programs on POWER9 processors
The strategy is directed by program characteristics which can be assessed by hardware performance counters
These strategies can take the form of compiler flags, source code pragmas/attributes
This talk addresses overall summary of options supported by open source compilers such as GCC, LLVM and IBM proprietary compilers such as XL
Tools used to measure performance counters- perf / PAPI

## Slide 4: POWER9 Processor
Optimized for Stronger Thread Performance and Efficiency
Increased Execution Bandwidth efficiency for a range of workloads including commercial, cognitive and analytics
Sophisticated instruction scheduling and branch prediction for unoptimized applications and interpretive languages
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation

## Slide 5: POWER9 Core Pipeline Efficiency
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation
Shorter Pipelines with reduced disruption
Improved Application Performance for Modern Codes
Advanced Branch Prediction
Higher Performance and Pipeline Utilization
  Removed instruction grouping
  Enhanced instruction fusion
  Pipeline can complete upto 128 (64-SMT4) instructions /cycle
Reduced Latency and Improved Scalability
  Improved pipe control of load/store instructions
  Improved hazard avoidance

## Slide 6: Tools Used in the Discussion
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation
Open source compilers such as GCC, LLVM and Proprietary compilers such as XL
  [gcc| clang | xlc] -O[n] program.c –o program for C programs
  [g++| clang++| xlC] -O[n] program.cc –o program for C++ programs
  Optimization level ranges from 0 to 3, Ofast for GCC, LLVM and upto O5 for XL
  Profile directed feedback
Perf tool
  To record hotspots/profile application
    perf record -e r<code> ./binary args > out (by default produces perf.data)
    perf report (opens profile report stored in perf.data)
  To measure hardware events
    perf stat –e r<code> ./binary args > out
  These counters can be read using PAPI API as discussed in the previous session

## Slide 7: Performance Tuning in the Front-End
Front end fetches and decodes the successive instructions and passes them to the backend for processing
POWER9 is a superscalar processor and is pipeline based so works with an advanced branch predictor to predict the sequence and fetch instructions in advance
However if there is a misprediction, it causes wrong path instructions to be fetched and introduces additional penalty as these instructions need to be flushed from the pipeline and correct instructions need to be fetched and processed
      Counters to detect this: PM_BR_MPRED*
Branches are caused even by function calls, Such branches affect instruction cache locality and increase instruction cache misses; Indirect function calls with no patterns make it difficult to predict with accuracy and can cause Instruction Cache Misses
  Counters to detect this: PM_L1_ICACHE_MISS
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation

## Slide 8: Tuning Strategies to improve Front End Performance- Unrolling
Unrolling loops (will reduce loop branches and in some cases branches within loop)
Manual unrolling in source
Language support to do unrolling in source
  Place #pragma unroll(N) before the for loop which needs to be unrolled
Compiler support for controlling Unrolling
  Enable Loop Unrolling: -funroll-loops: Leave it to the compilers judgement to decide optimal unrolling for each loop
  Disable Loop unrolling : -fno-unroll-loops
int x;
for(x=0;x<100;x+=5) {
func(x);
func(x+1);
func(x+2);
func(x+3);
func(x+4);
}
int x;
for(x=0;x<100;x++)
{
func(x);
}
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation

## Slide 9: Tuning Strategies to improve Front End Performance- Inlining
Shorter routines are best to be inlined to avoid call overhead and reduce branches
Broadens the window available for better scheduling
Manual function inlining in source
Language Support– use inline __attribute__((always_inline)) in front of a function definition
Compiler Support
  -finline-functions(GCC, LLVM), -qinline(XL) : Inline suitable functions
  Compiler supports inlining thresholds : number of instructions in a function before it can be considered for inlining
Help Compiler to Inline more Functions:
  Convert Indirect calls to direct calls
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation

## Slide 10: Tuning Strategies to improve Front End Performance
If you have a branch that assigns a different value depending on a condition we can convert it to a one line assignment statement with the ?: operator
Compiler generates isel instructions for such branches that essentially converts a control dependency into a data dependency
GCC/LLVM option to generate isel : -misel. To Disable generation of isel: -mnoisel
For simple branches as below, we may leave the branch statement as it is; The branch predictor will automatically take care of the performance
Other techniques to improve performance: Provide hints in source code to indicate the expected values of expressions appearing in branch conditions (long __builtin_expect(long expression, long value);) (hint whether branch is more likely to be taken/not)
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation
a=(val==M)?b:c;
If(val==M) a=b; else a=c;
If(val>M) M=val;

## Slide 11: Tuning Strategies to Improve Backend Performance
Backend of the processor is concerned with execution of the instructions
There are numerous ways we can tune performance in the backend
  Using Processor Resources effectively-
    Registers,
    Caches,
    Prefetching
  Vectorization
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation

## Slide 12: Using Processor Registers Effectively
CPU Registers are an important resource for execution and are finite in number
Compiler has to judge and allocate variables into registers to avoid spilling as much as possible
Spill is a mechanism when a register value is saved on to memory for later use as the register is required to do some thing else
Each spill will require one store + a future load (to use that value from memory)
If distance between store and load is short it may cause a dependency chain in the pipeline
Stalls due to spills can be detected using the following counters- PM_LSU_FIN, PM_LSU_FLUSH,
Use other register resources like SIMD registers if applicable (Vectorization)
Use multipurpose instructions such as andc (logical AND complement), orc (logical OR complement) which combines multiple math operations in a single instruction saving a register,
Record instructions such as addi. That does the operation and also set the CR fields
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation

## Slide 13: Using Caches Effectively
Memory is organized in a hierarchy
L1 cache : Closest memory to the processor and the fastest, followed by L2, L3 upto Memory
Memory is most distant to the processor and slowest
Data cache : stores data, instruction cache: stores instructions
Data cache misses can stall load instructions in the pipeline causing a cascading effect on all those instructions dependent on it data
Counters- PM_LD_MISS_L1, PM_CMPLU_STALL_DCACHE_MISS, PM_ST_MISS_L1, PM_CMPLU_STALL_DMISS_L2L3, PM_CMPLU_STALL_DMISS_LMEM etc
Memory
(~300+ cyc)
L3 $
(~26 cyc)
L2 $
(~10 cyc)
L1 $
(~3 cyc)
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation

## Slide 14: Memory footprint reduction (enum=small)
Use only as much memory as required
Game applications such as chess, GO contain data structure to represent board
Each square has a fixed number of states, n, which is usually a single digit number
Usually such a data type is defined as an enumerated data type such as
  typedef enum {BLACK=0, WHITE=1,…} square;
Typically each element of square will be allocated as
type “int” (4 bytes)
Compile the application with –qenum=small(XL) or –fshort-enums(LLVM,
GCC) that allocates only minimum required memory to store each
element of square (1 byte),
1/4th memory will be used
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation

## Slide 15: Prefetching
Hardware prefetching
  Controlled by DSCR (data stream control register) settings;
    –ppc64_cpu --dscr=<n>
  Common DSCR configurations: n=0 (moderate depth, ramp) : By default the HW prefetcher is “ON”
  n=0x1D7 (Achieve most aggressive depth, most quickly, enable stride N prefetch),
  n=0x1 (no prefetch)
  Reference: https://developer.ibm.com/linuxonpower/docs/linux-on-power-application-tuning/
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation

## Slide 16: Software Prefetching
Programmer inserted prefetch instructions __dcbt (load prefetch), __dcbtst (store prefetch)
If you want to explicitly control prefetching via software *only*, you can turn off hardware prefetching using
    ppc64_cpu –dscr=1
Compilers provide an option to enable compiler to insert prefetch instructions wherever applicable. However this is only a directive that can be ignored by the compiler if it does not see adequate benefit
XL: (-qprefetch/-qnoprefetch) and GCC (-fprefetch-loop-arrays/-fno-prefetch-loop-arrays); Some compilers such as GCC may include further loop optimizations when –fprefetch-loop-arrays is invoked.
XL/POWER9 supports setting DSCR values at compile time for an application
Example: -qprefetch=dscr=<value>
Compiling with the option –qprefetch=dscr=7 sets the prefetch level to 7
Compiling with the option –qprefetch=dscr=1 turns off hardware prefetching and is equivalent to
ppc64_cpu –dscr=1
Useful in cases where we cannot obtain root privileges to play with prefetch settings on the command line
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation

## Slide 17: Vectorization
Compute intensive programs whose computations can be parallelized can take advantage of vector instructions on POWER
    Advantages- reduces loads, stores and hence pathlength, reduces register pressure on GPRs, effective use of resources, Faster throughput
At a time- Vector instructions can work on 4 32 bit words, 8 half-words and 16 bytes
  Amount of work done per unit time correspondingly becomes faster
Clang/GCC: -ftree-loop-vectorize, -mvsx, -maltivec, -mllvm –force-vector-width=n(Clang only),
Help the Compiler to automatically vectorize loops
    Keep the loop simple
    Avoid extensive branches, pointer references within loops (use restrict wherever applicable)
  GPU codes can scale really well with SIMDization for performance
    Structure of arrays are more amenable to vectorization than array of structures

## Slide 18: Additional Ways to Improve Performance
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation
Serial v/s Parallel Execution: tasks that don’t have dependencies can be done in parallel using a framework such as OpenMP that can perform Tasks in 1/Nth time with N threads
If Mathematical accuracy is not important, use -Ofast
  This automatically substitutes expensive library calls to native implementation of the math function using target ISA
Thread Binding
  We can use OMP_PLACES=“{0},{5},{10},{15}" OMP_NUM_THREADS=4 time ./application <params> to bind first thread to CPU0, second thread to CPU1, … so on
  For GCC specific applications, we can use GOMP_CPU_AFFINITY="0 5 10 15" that inturn sets OMP_PLACES
  The ordering of CPU numbers determines performance of the application
  If all threads are bound to a single CPU execution speed slows down
  To choose the right CPU number on a POWER Linux system, we can consult the file /sys/devices/system/cpu/cpu0/topology/thread_siblings_list
Large Pages- allow TLB to map to a larger virtual memory page thereby reducing TLB misses. Memory intensive applications that use large amounts of virtual memory can benefit with using largepages

## Slide 19
Flag Kind | XL | GCC/LLVM | Can be simulated in source | Benefit | Drawbacks
Unrolling | -qunroll | -funroll-loops | #pragma unroll(N) | Unrolls loops ; increases opportunities pertaining to scheduling for compiler | Increases register pressure
Inlining | -qinline=auto:level=N | -finline-functions | Inline always attribute or manual inlining | increases opportunities for scheduling; Reduces branches and loads/stores | Increases register pressure; increases code size
Enum small | -qenum=small | -fshort-enums | -manual typedef | Reduces memory footprint | Can cause issues in alignment
isel instructions |  | -misel | Using ?: operator | generates isel instruction instead of branch; reduces pressure on branch predictor unit | latency of isel is a bit higher; Use if branches are not predictable easily
General tuning | -qarch=pwr9, -qtune=pwr9 | -mcpu=power8, -mtune=power9 |  | Turns on platform specific tuning | 
64bit compilation | -q64 | -m64 |  |  | 
Prefetching | -qprefetch[=aggressive] | -fprefetch-loop-arrays | __dcbt/__dcbtst, _builtin_prefetch | reduces cache misses | Can increase memory traffic particularly if prefetched values are not used
Link time optimization | -qipo | -flto , -flto=thin |  | Enables Interprocedural optimizations | Can increase overall compilation time
Profile directed feedback | -qpdf1, -qpdf2 | -fprofile-generate and –fprofile-use LLVM has an intermediate step llvm-profdata |  | Enables hot path optimizations | Requires a training run

## Slide 20
Summary
Today we talked about
  Tuning strategies pertaining to the various units in the POWER9 HW –
    Front-end, Back-end
    Some of these strategies were compiler flags, source code pragmas that one can apply to see improved performance of their programs
  We also saw additional ways of improving performance such as parallelization, binding etc
  During the presentation we were introduced to several POWER9 PMU counters that helps us understand bottlenecks of performance
    Get counter data either using perf stat or PAPI APIs
  We concluded with a comparison of compiler flags on open source compilers such as GCC, LLVM with IBM XL compilers
IBM Systems / version 1.0 / November, 2019 / © 2018 IBM Corporation
Disclaimer: This presentation is intended to represent the views of the author rather than IBM and the recommended solutions are not guaranteed on sub optimal conditions